## Slide 1: IoT for the Enterprise
Big Data Ignite 2017
Slides at https://www.loouq.com/blog
Events (right margin)
Notes: Introduction and any housekeeping
In the 45 minutes we have today
  More questions than answers
Hope everyone leaves ready to approach their IoT project with a new set of ideas

## Slide 2: Why Do IoT?
Data Changes Perspective
This is the fundamental value proposition behind IoT
Device control is valuable, but data drives IoT
With Transparent Data Exchange We Change Processes
More accurate
Less time
Transparent transactions
Notes: Quick survey… who’s doing an IoT and why
If no good examples talk to
Parking Occupied
Automatic replenishment
  Customer engagement
  Offer discounts, free device
  Win-win scenario

## Slide 3: IoT Implementation Challenges
Cross Disciplinary
1
Operation Technology Driven
Information Technology Dependent
Uncharted Waters
2
Security
Data Ownership and Privacy
New Skills for Most Enterprises
3
Notes: Neither operational technology or information technology teams can do it alone
IoT skills are diverse if you roll you own from start to finish lot to learn
Devices are unique
IoT is built for cloud data centers, and many organizations are still getting their arms around cloud
Enterprise developers understand service integration, “glue code” and enterprise applications
Less confident with real time events, queue, device twin/mirrors
Java/C# vs. C/C++

## Slide 4: IoT Device Constraints
IoT devices are limited in…
Computing power
Memory
Communications options
Power
Device selection involves careful identification of project objectives first
Who consumes the device data?
Where is the device located?
If embedded, what are the characteristics of the host device\machine?
Notes: SOM/SOC or board
Boards build on CPU chip
SOM/SOC usually have some communication integrated (ESP32 ESP8266)
ST BlueNRG has embedded Cortex M0 core
SOM and many development boards are
256 K flash or less
24K or 32K of RAM
How will device be powered?
  Coin cell
  Li-Ion, Li-Poly
  Solar cell

## Slide 5: Pick Two
Notes: Pick 2 sums it up, you cannot get all 3
While this is directly tied to communication technologies, this decision is the essentially the core question of IoT projects
What is your physical host?
What is its power, space, location, size?

## Slide 6: Communications
Ethernet
  POE potential help
  SSL processing creates challenges for device capabilities
GSM\CDMA
  Quickly becoming outdated in North America. Legacy infrastructure being powered down. Still via in some parts of the globe Risky for any new project
Wi-Fi
  Wi-Fi modules are for the most part FCC pre-certified and off-load SSL\TLS duties from host device processor
LoRa / LoRaWAN
  Long-distance, low-power, low-bandwidth
  Semtech / LoRa Alliance
  8-10 kilometer range
Sigfox
Similar to LoRaWAN
Semtech (LoRa) sells chips
SigFox sells network access
5G Cellular
  LTE CAT-M1
  NB-IoT
  3GPP Release 15
  For IoT 5G cellular is an evolution and primarily a network operator shift
Notes: Tied for importance with CPU options
A couple are on the decline, avoid for future
Pushing the envelope to emerging may offer challenges, but consider your intended application life
How hard is it to replace devices, changing communications technology is not a firmware update
Regardless of radio technology module only
FCC certification is expensive and time consuming

## Slide 7: Application Protocols
AMQP
HTTP
There are others CoAP, LWM2M, etc.
  Implementations?
MQTT
Notes: For the most part this issue will be answered for you
Platform or toolkit SDK will likely spec out
MQTT is winning this race… thin enough for IoT device implementation, doesn’t have the overhead of AMQP, better model that HTTP
Not aware of any of the IoT specific protocols have large implementation

## Slide 8: IDE Options
Likely different than you are used to
Visual Studio and Eclipse option for some platforms
Mbed (IDE, platform, ecosystem)
PlatformIO
Other “embedded” tool-chains are usually expensive
http://docs.platformio.org
Notes: One of the key areas where enterprise developers will feel “outside”
Will likely be driven by other project choices
Development boards vs. Evaluation Boards
Toolchains
GCC \ GNU
MDK-ARM - Keil
Crossworks - Rowley
Visual Studio - Visual Micro and VisualGDB

## Slide 9: Debugging Device Applications
Different approach required
Layer up, test frequently
Exception management: exception not the rule
Consider hardware debugger options
Evaluation Kits
Embedded debugger + probe
(Segger J-Link)
Integrated debugger (Arduino Zero)
Notes: Huge difference from debugging server/workstation or C#/Java
Hardware debugger really required for reasonably productivity

## Slide 10: Watchdog Processes
For unattended applications consider implementing a watchdog function
Software vs. Hardware Watchdogs
Notes: Some devices\SOCs have embedded WD
Hardware is preferred if possible,
software WD are susceptible to software failures, which is what the WD is protecting us from

## Slide 11: Security
Devices are not powerful and cannot defend themselves
  Minimize attack surface
  Minimize trust
  Security by obscurity is neither
1
Service Assisted Communications
  Clemens Vasters (Microsoft)
  https://blogs.msdn.microsoft.com/clemensv/service-assisted-communication-for-connected-devices2014/02/09//
2
Senate recognized security concerns: Internet of Things Cybersecurity Improvement Act of 2017
Several recent high-profile exploits (consumer products)
Now famous 60 Minutes car-hacking
https://www.youtube.com/watch?v=rGMdmA9gqzc
3
Notes: Does everyone know what “attack surface” means
Devices are in a hostile environment, they cannot analyze attack vectors
Trust only what is absolutely necessary to perform device functions

## Slide 12: Platforms
All platforms are not created equal
Diverse set of services offered
Device management
Data communications
Storage
Security
Application Features
Notes: Many device mfg have platforms that are centered only on device management
Microsoft and AWS “platforms” are really just components targeting ingestion and security

## Slide 13: Buy Where You Can, Build Where You Must
Components by Project Timeline
  Proof of Concept\Prototype
    Development boards (Arduino, Raspberry PI, Adafruit, DragonBoard)
    Select development boards hosting technologies you need
    Create custom circuitry for sensors\actuators only
    Modularize and abstract hardware specific code
  Pilot
    Continue to use standard development boards
    Consider alternate production sources (most are open source) to ensure supply chain
Notes: This slide presents one possible (LooUQ recommended approach) to building up an IoT project

## Slide 14: Thank You
Greg Terrell
CEO
LooUQ Incorporated
East Lansing, MI 48823